## Slide 1: Pathways to Commercial Liftoff Virtual Power Plants Update
January 2025

## Slide 2: Since the VPP Liftoff Report was published in September 2023, the near-term pressures on the U.S. electric grid have intensified
Rapid electricity demand growth
Reliability
Upward pressure on customer costs from growing capital investments
Affordability
Increasingly frequent extreme weather events
Resilience

## Slide 3: Reliability: Peak demand is growing faster than anticipated; projections show peak rising by ~100 GW between 2024 and 2030
Chart: 
| 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
 | 11.6201 | 14.4599 | 29.1854 | 48.7905 | 70.2588 | 86.6636 | 98.5267 | 108.4335
 | 3.8463 | 9.7029 | 19.2969 | 27.6118 | 37.33 | 44.6811 | 50.7044 | 57.8909
 | 8.8008 | 15.23 | 20.4517 | 25.2277 | 29.918 | 32.9355 | 38.3045 | 44.2598
0
800
810
820
830
840
850
860
870
880
890
900
2024 Projection
2023 Projection
2022 Projection
U.S. summer peak hour demand by year (2023-2030), GW
Source: NERC 2024 Electricity Supply and Demand data

## Slide 4: Affordability: Growth in distribution system costs outpaces all other grid capital costs
Chart: 
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
 | 22048931196.6718 | 14191662808.2839 | 16010900752.4631 | 13720946657.8042 | 24306155314.6068 | 28657954853.448 | 33867880422.6644 | 29280967925.0467 | 29417393158.9918 | 36732053835.0862 | 24445454739.2664 | 34083267121.2153 | 33394165838.2059 | 30724131636.0205 | 19299802523.7634 | 33033684601.241 | 37655701087.5889 | 28400870703.1384 | 22508175195.8055 | 20693415089.6633 | 25350804797
 | 6261540389.1415 | 6357644632.6851 | 6841837779.5259 | 10340663506.0868 | 9805848276.433 | 12334948897.466 | 12416590021.3567 | 14594798593.5995 | 14492857483.3393 | 18600391894.2834 | 22499159106.4995 | 25094317923.8632 | 25219605218.5408 | 26346931292.1248 | 24016621788.3036 | 27305445855.7197 | 27569394717.706 | 30563016279.0972 | 27974949853.6015 | 25004944674.534 | 27659625796
 | 19591545946.2 | 20649555184.3804 | 20873749155.9235 | 24339362291.2276 | 22711753647.3118 | 24676839836.0672 | 24015610054.8825 | 23011693711.9916 | 23266059855.6724 | 25962940850.0513 | 24089447222.6643 | 26658596306.5202 | 29127561725.8367 | 30707096067.6946 | 32330209591.2399 | 35649788331.944 | 39235740304.0734 | 42863906712.4699 | 43704607586.885 | 44427842124.3358 | 50945100524
 | 4886156265.7686 | 4021742700.3474 | 3917239180.4369 | 3223870377.0678 | 3757407764.8437 | 4810263809.5501 | 5058026971.3625 | 5105758827.0997 | 5605746983.0859 | 6439118802.5436 | 5740644950.7492 | 6459409737.1176 | 6602857749.495 | 7440081423.8627 | 8657072301.871 | 8323299809.4328 | 10640480504.1949 | 9867850840.0344 | 11513590099.3149 | 11417964937.6791 | 12707043967
0
5
10
15
20
25
30
35
40
45
50
55
Generation
Transmission
Distribution
Other
Annual U.S. capital expenditures by sector (2003-2023), billions of 2023 U.S. dollars ($)
Source: FERC Form 1 (Electric Utility Annual Report)

## Slide 5: Resilience: The number of billion-dollar climate and weather events has doubled over the last 10 years
Chart: 
 | 5 | 3 | 6 | 7 | 6 | 6 | 8 | 5 | 12 | 9 | 7 | 18 | 11 | 10 | 10 | 11 | 15 | 19 | 16 | 14 | 22 | 20 | 18 | 28 | 24
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024 YTD (as of Oct)
Number of billion-dollar climate and weather events, count / year (adjusted for inflation)
Source: NOAA Billion-Dollar Weather and Climate Disasters

## Slide 6: Against the backdrop of these challenges, VPPs are among the critical solutions that can ensure a reliable, affordable, resilient grid
Basic VPPs can be launched in less than 6 months
Quick to deploy
VPP peaking capacity is 40% cheaper than a traditional power plant
Low-cost
Solar with batteries and / or fuel generator VPPs can provide backup power during emergencies
Resilient

## Slide 7: Recall: What is a virtual power plant (VPP)?
Reference the 2023 VPP Liftoff Report for additional background

## Slide 8: Quick to deploy: Basic VPPs that provide valuable peak shaving capabilities can be implemented in less than six months
Timeline to add 20 MW of dispatchable peaking capacity, months
Chart: 
 | 6 | 27 | 20
 | 6 | 23 | 40
Basic VPP
Utility scale battery
Gas peaker plant
6-12 months
27-50 months
20-60 months
Time required to add capacity (25th percentile)
Additional time that may be necessary depending on local constraints (75th percentile)
Legend
Source: Industry interviews, RMI Reliability Brief, Lawrence-Berkeley National Lab’s 2024 Queued Up Report

## Slide 9: Lower-cost: Net cost to a utility of providing resource adequacy from a VPP can be 40% to 60% lower cost vs. alternatives
Comparison of net cost to an example utility of providing 400 MW resource adequacy across three options, Net cost per kW-year
Chart: 
 | 42.84 | 68.68 | 99.12
Basic VPP
Utility scale battery
Gas peaker plant
$43
$69
$99
Source: Brattle Group’s Real Reliability: The Value of Virtual Power Report

## Slide 10: Deploying 80-160 GW of VPPs by 2030 (enough to serve 10-20% of peak load) could support rapid load growth while reducing overall grid costs
Chart: 
| 2024 | Demand served from retiring assets | New capacity needed to meet peak demand | 2030
 | 0.03736 | 0.13378
Demand served by non-VPP generating capacity | 773 | 777
Demand served by VPP capacity | 30 | 120
 | 703 | 703
Demand served from retiring assets | 100
New capacity needed to meet peak demand | 194
US Peak electricity demand
~800 GW
~900 GW
~200 GW peak demand needs
~100 GW potential retirements
2024 Current state
2030 VPP Liftoff
~30 GW VPPs
Peak demand served by VPPs
Peak demand served by retiring resources
Peak demand served by non-VPP resources
New resources needed to meet peak demand
80-160 GW VPPs by 2030
10-20% of peak
~3-5x current scale
VPP liftoff
Source: NERC 2024 Long-Term Reliability Assessment, NERC 2024 Electricity Supply & Demand data, Wood Mackenzie 2024 NA VPP Market Report

## Slide 11: Recall: Five imperatives will accelerate Liftoff for VPPs
Expand DER adoption with equitable benefits
Simplify VPP enrollment
Increase standardization in VPP operations
Integrate into utility planning and incentives
Integrate into wholesale markets
1
2
3
4
5

## Slide 12
Expand DER adoption with equitable benefits
Simplify VPP enrollment
Increase standardization in VPP operations
Integrate into utility planning and incentives
Integrate into wholesale markets

## Slide 13: Example in action: Solar Battery Savings program
Case study: San Diego Community Power, CA |  | 
San Diego Community Power leverages upfront, stackable incentives to provide the opportunity for no-cost solar and batteries to qualified priority populations |  | 
The program was designed to benefit all customers through upfront incentives for solar and batteries | Community Power worked with state and local programs to ensure their incentives could stack with other programs | 

## Slide 14
Expand DER adoption with equitable benefits
Simplify VPP enrollment
Increase standardization in VPP operations
Integrate into utility planning and incentives
Integrate into wholesale markets

## Slide 15
Maine is estimated to have over 2 GW of dispatchable capacity by 2030, with ~50% coming from fuel generators and the remaining from EV chargers, heat pumps, and smart thermostats.
Texas is estimated to have 16.5 GW of dispatchable capacity by 2030, a third of which comes from EV chargers. The remaining comes primarily from C&I loads, smart thermostats, and heat pumps.
2030 total dispatchable capacity, GW
DER capacity is expected to grow in every state across the U.S., though the magnitude of growth and the types of DERs that come online will vary
California is estimated to have over 50 GW of dispatchable capacity by 2030, spread out across all DER types. EV chargers, fuel generators, and batteries comprise the majority.
Source: Ohm Analytics State-Level Residential DER Capacity Forecast, Wood Mackenzie 2024 US DER Market Report, National Renewable Energy Lab The 2030 National Charging Network Report, EIA 2022 Meter Data, DOE analysis

## Slide 16: 10-20% of peak demand could be served by VPPs with baseline forecasts of DER adoption and demonstrated best-in-class VPP enrollment rates
Assumptions |  | ~15% of dispatchable capacity additions only | ~15% uplift from improved messaging, flexibility, and customer value proposition | ~30% uplift from point-of-purchase enrollment; additional upside from automatic enrollments with opt-outs
Chart: 
 | 30 | 30 | 56.41 | 82.82 | 82.82
 | 26.41 | 26.41 | 30 | 80
 | 50
2024 VPP capacity
~25
Current VPP enrollment rate
~25
No-regrets enrollment practices
~30
~50
Proven high-impact enrollment practices
2030 VPP capacity
~30 GW
~30-65
~80-160 GW
Enrollment rate assumed |  | ~15% | ~30% | ~60%-90%
Source: DOE analysis

## Slide 17
Expand DER adoption with equitable benefits
Simplify VPP enrollment
Increase standardization in VPP operations
Integrate into utility planning and incentives
Integrate into wholesale markets

## Slide 18: In the past year, DOE and other industry actors have launched or expanded efforts to standardize critical areas of VPP operations
Distribution system operators
VPP platforms
Customer DERs
Focus area of recent standardization efforts | Example initiatives (not exhaustive)
VPP platform to utility communication interface | FlexIT
Grid services definitions | DOE Distribution System Transformation
Aggregator service contracts | NAESB standard services contract
VPP platform to DER communication interface | Mercury Consortium
Meter data format and access rules | Green Button Standard
VPP resource definition | IEEE VPP Guide
Shared DER registry | CULSN DER registry model
Cybersecurity for DERs | DER Cybersecurity Best Practices
1
2
3
4
5
6
7
8

## Slide 19
Expand DER adoption with equitable benefits
Simplify VPP enrollment
Increase standardization in VPP operations
Integrate into utility planning and incentives
Integrate into wholesale markets

## Slide 20: VPP deployment has been highest in states where state regulators and policymakers have implemented VPP-supportive actions
Number of VPP deployments vs state policy/regulatory VPP-related actions (2020-Q3 2024), count
Source: Wood Mackenzie 2024 NA VPP Market Report, North Carolina Clean Energy Technology Center Policy & Regulatory Actions

## Slide 21
Expand DER adoption with equitable benefits
Simplify VPP enrollment
Increase standardization in VPP operations
Integrate into utility planning and incentives
Integrate into wholesale markets

## Slide 22: ISO/RTO compliance with FERC Order 2222 requirements has been varied: CAISO, NYISO, and ISO-NE are leading implementation
Issue Areas | CAISO | ISO-NE | NYISO | PJM | MISO | SPP
Metering and Telemetry System Requirements |  |  |  |  |  | 
Participation Model |  |  |  |  |  | 
Double Counting of Services |  |  |  |  |  | 
Locational Requirements |  |  |  |  |  | 
Role of Distribution Company |  |  |  |  |  | 
Ongoing Operational Coordination |  |  |  |  |  | 
Small Utility Opt-in |  |  |  |  |  | 
Interconnection |  |  |  |  |  | 
Definitions of DER and DER Aggregator |  |  |  |  |  | 
Types of Technologies |  |  |  |  |  | 
Allow a DER to serve as its own aggregator |  |  |  |  |  | 
Min and Max Size of Aggregation |  |  |  |  |  | 
Min and Max Size for DER in an Aggregation |  |  |  |  |  | 
Distribution Factors and Bidding Parameters |  |  |  |  |  | 
Information and Data Requirements |  |  |  |  |  | 
Role of RERRA |  |  |  |  |  | 
Modifications to List of Resources in Aggregation |  |  |  |  |  | 
Market Participation Agreements |  |  |  |  |  | 
Demand response opt-out |  |  |  |  |  | 
Source: Lawrence Berkeley National Lab DER Participation in Wholesale Markets Report, FERC filings

## Slide 23: Five imperatives will accelerate Liftoff for VPPs
Expand DER adoption with equitable benefits
Simplify VPP enrollment
Increase standardization in VPP operations
Integrate into utility planning and incentives
Integrate into wholesale markets
1
2
3
4
5
Adopting and adapting demonstrated best practices and leveraging existing tools and resources can accelerate deployment to address near-term grid needs

## Slide 24: Thank you!
The 2025 VPP Liftoff Update can be found at liftoff.energy.gov/vpp
Feedback is welcome at liftoff@hq.energy.gov
75+ real-world case studies
60+ new DOE and industry resources
Link to the report!